Laboratory 2.9.1

Name

Department

Software Engineering

Group

____

Packet Tracer - Basic Switch and End Device Configuration

Addressing Table

| Device | Interface | IP Address | Subnet Mask |
| --- | --- | --- | --- |
| Class-A | VLAN 1 | 128.107.20.10 | 255.255.255.0 |
| Class-B | VLAN 1 | 128.107.20.15 | 255.255.255.0 |
| Student-1 | NIC | 128.107.20.25 | 255.255.255.0 |
| Student-2 | NIC | 128.107.20.30 | 255.255.255.0 |

Objectives

- Configure hostnames and IP addresses on two Cisco Internetwork Operating System (IOS) switches using the command-line interface (CLI).

- Use Cisco IOS commands to specify or limit access to the device configurations.

- Use IOS commands to save the running configuration.

- Configure two host devices with IP addresses.

- Verify connectivity between the two PC end devices.

Scenario

As a recently hired LAN technician, your network manager has asked you to demonstrate your ability to configure a small LAN. Your tasks include configuring initial settings on two switches using the Cisco IOS and configuring IP address parameters on host devices to provide end-to-end connectivity. You are to use two switches and two hosts/PCs on a cabled and powered network.

Instructions

Configure the devices to fulfill the requirements below.

Requirements

- Use a console connection to access each switch.

•	Name Class-A	and	Class-B	switches.

- Use the R4Xe3 password for all lines.

•	Use the C4aJa	secret password.

- Encrypt all clear text passwords.

- Configure an appropriate message-of-the-day (MOTD) banner.

- Configure addressing for all devices according to the Addressing Table.

- Save your configurations.

- Verify connectivity between all devices.

Note: Click Check Results to see your progress. Click Reset Activity to generate a new set of requirements.

If you click on this before you complete the activity, all configurations will be lost.

End of Document

Conclusion