## Slide 1: Review on SC for seminars
Part I

## Slide 4: Densitatea stărilor
Funcția de distribuție

## Slide 5: Legile statisticii ...
Maxwell-Boltzmann funcția de probabilitate
Nu sunt limite pentru nr de particule pe fiecare stare de energie, dar permite particulele in gaze
Bose – Einstein –
Nu sunt limite pentru nr de particule pe fiecare stare de energie, dar nu permite identificarea unei particule
Fermi – Dirac
Da, pentru electroni in cristale.
O particule pentru un nvel de energie

## Slide 6: Fermi-Dirac distribuția

## Slide 7: Densitatea stărilor
The density of electrons (no) can be found precisely if we know
  1. the number of allowed energy states in a small energy range, dE: S(E)dE
    “the density of states”
  2. the probability that a given energy state will be occupied by an electron: f(E)
  “the distribution function”
no = bandS(E)f(E)dE

## Slide 8
For quasi-free electrons in the conduction band: 1. We must use the effective mass (averaged over all directions) 2. the potential energy Ep is the edge of the conduction band (EC)
For holes in the valence band: 1. We still use the effective mass (averaged over all directions) 2. the potential energy Ep is the edge of the valence band (EV)
conduction band
valence band
EC
EV
x
E(x)
S(E)
note: increasing electron energy is ‘up’, but increasing hole energy is ‘down’.

## Slide 9: Distribuția Fermi-Dirac
The probability that an electron occupies an energy level, E, is
f(E) = 1/{1+exp[(E-EF)/kT]}
  where T is the temperature (Kelvin)
  k is the Boltzmann constant (k=8.62x10-5 eV/K)
  EF is the Fermi Energy (in eV)
f(E)
1
0
EF
E
T=0 oK
T1>0
T2>T1
0.5
All energy levels are filled with e-’s below the Fermi Energy at 0 oK

## Slide 10
for electrons, n(E)
for holes, p(E)

## Slide 11: Energy Band Diagram for intrinsic semiconductor n0=p0=ni
where Ei is the intrinsic Fermi level

## Slide 12: Energy Band Diagram for:
is independent of the Fermi Energy
for all non-degenerate semiconductors.
(that is as long as EF is not within a few kT of the band edge)

## Slide 13: The intrinsic Fermi Energy (Ei)
The intrinsic carrier density
is sensitive to the energy bandgap, temperature, and m*
no=po and EF=Ei
which gives
Ei = (EC + EV)/2 + (kT/2)ln(NV/NC)
so the intrinsic Fermi level is approximately
in the middle of the bandgap.

## Slide 16: T dependence of e- & e+ concentrations

## Slide 17: Eg vs T

## Slide 18: Doped materials> Materials with impurities!

## Slide 19: Doped materials

## Slide 21: Al doilea mod de distinctive dintre material conductoare si semiconductoare

## Slide 24: concentraţiile purtătorilor de sarcină în semiconductoarele extrinseci
De tip n (ND >> ni; NA = 0
purtatori majoritari
purtatori minoritari
De tip p (NA >> ni; ND = 0
Natura purtătorului de sarcină
tipul semiconductorului
la echilibru termic

## Slide 25: Statistica donorilor si acceptorilor