## Slide 1: Tema Concepte și Terminologie în Metrologie Metrologia cuantică
Company Name

## Slide 4
Since ancient times mankind was aware that there are certain quantities that are measurable, i.e., that can be compared
Measurements have been based on artefacts over thousands of years, most prominently, the international prototype of the kilogram, the IPK
In 2018, the General Conference on Weights and Measures, CGPM, abolished all artefacts in a revolutionary decision defining the Inter- national System of Units, the SI, by fixing the numerical values of 7 defining constants
h = 6,626 070 15 × 10 - 34 J ⋅ s

## Slide 5: Moldova
Units of Measurement
Standards
Measuring Instruments
Essential to fundamental research
Highly accurate measurements
Reduced uncertainty
Developing new and better measurement capabilities
Scientific progress

## Slide 6: National Metrology
the National Metrology Institution develops activities in the fields
Scientific Metrology - assures the realization and implementation of the SI units and national standards
Applied Metrology - assures the national traceability chain of measurement reference & industrial standards of accredited laboratories
Legal Metrology - is the national authority to assure and manage the legal metrological control system of the measuring instruments of current measurements-final users

## Slide 7: Joint Committee for Guides in Metrology
VIM: International Vocabulary of Metrology
www.bipm.org/en/committees/jc/jcgm/publications
GUM: Guide to the Expression of Uncertainty in Measurement
SI Brochure: The International System of Units (SI)

## Slide 8
International vocabulary of metrology – Basic and general concepts and associated terms (VIM)
  – measurement: process of experimentally obtaining one or more quantity values that can
reasonably be attributed to a quantity
    Measurement does not apply to nominal properties.
    Measurement implies comparison of quantities or counting of entities.
    Measurement presupposes a description of the quantity commensurate with the intended use of a measurement result, a measurement procedure, and a calibrated measuring system operating according to the specified measurement procedure, including the measurement conditions.
2.13 - measurement accuracy: closeness of agreement between a measured quantity value
and a true quantity value of a Measurand
A measurement is said to be more accurate when it offers a smaller measurement error.

## Slide 9
Indication of Measuring Instrument
Error
True Value
Uncertainty
2.16 - measurement error
measured quantity value minus a reference quantity value
International vocabulary of metrology – Basic and general concepts and associated terms (VIM)
2.17 - systematic measurement error
component of measurement error that in replicate measurements remains constant or varies in a predictable manner
2.19 - random measurement error
component of measurement error that in replicate measurements varies in an unpredictable manner

## Slide 10
International vocabulary of metrology – Basic and general concepts and associated terms (VIM)
2.26 - measurement uncertainty
non-negative parameter characterizing the dispersion of the quantity values being attributed to a
measurand, based on the information used
2.9 - measurement result
set of quantity values being attributed to a measurand together with any other available relevant Information
Y = y ± U
mS = (100,021 ± 0,035) g

## Slide 11
2.16 – metrological traceability
property of a measurement result whereby the result can be related to a reference through a documented unbroken chain of calibrations, each contributing to the measurement uncertainty measured quantity value minus a reference quantity value
Metrological traceability requires an established calibration hierarchy.
International vocabulary of metrology – Basic and general concepts and associated terms (VIM)

## Slide 12: The fiew SI

## Slide 13: International System of Units
The new International System of Units (SI) officially approved on November 2018 following 26th General Conference of Weights and Measures (CGPM), the highest body of the Meter Convention of which Portugal is a founding signatory (1875) and adopted in 20th May 2019.
New Paradigm Change - new definitions use “explicit constant” formulation (instead of “explicit unit”), which allows separate the definition from the realisation of the units, based on the physics equations;
New SI is called as Quantum SI  units are defined considering microscopic
properties and considering the quantum nature of phenomena
 the previous definition of kg – based on an artefact consisting of many atoms →
is now replaced by the definition using Planck constant h
Objective
More accurate and rigorous Measurement System
And to Support
Science, Research and Technological Developments

## Slide 14: International System of Units
New SI – 26th CGPM
Definition of units
through fundamental
constants
New Definition
New Definition
New Definition
1st CGPM
Evolution of the SI
International System of Units (SI) - system of units, used around the world as the preferred basic language for science, technology, industry and trade since it was established in 1960 by a resolution at the 11th meeting of the General Conference on Weights and Measures (CGPM) of BIPM
– it has been periodically updated
- to keep up with the science developments and answer the need for more accurate measurements and in the new technical domains;
- unique and Coherent
- ensures the worldwide uniformity of Measurement and Traceabilityty

## Slide 15: International System of Units
– But ... the seven base units of the SI, the kg was still defined (based) in terms of the mass of an artifact  international prototype of the kilogram IPK, kept in the BIPM - which is not stable ....
IPK - international prototype of the kilogram (platinum-iridium alloy)
Drift observed in the six copies of the international kilogram prototype (comparisons in 1889, 1946, 1991 e 2014 ) 50 µg

## Slide 16: International System of Units
Definition of the unit of measure
Material measures
e.g. International prototype
of kilogram
e.g. International prototype of kilogram
Material parameters
e.g. Triple point of water – to
define the kelvin
e.g. Triple point of water – to define the kelvin
Ideal experimental
prescriptions
e.g. Ideal situation to define
ampere and candela
e.g. Ideal situation to define
ampere and candela
Fundamental constants
e.g. Speed of light in vacuum,
c, to define the metre
e.g. Speed of light in vacuum,
c, to define the metre
Until November 2018:

## Slide 17: International System of Units
A
cd
K
mol
m
kg
s
Situation in 2018 – before 26th General Conference on Weights and Measures
- 3 definitions based on fundamental constants (or conventional values)
metre (c)
ampere (μ0)
candela (Kcd)
- 3 definitions based on the properties of materials
second (133Cs)
kelvin (H2O)
mole (12C)
1 definition based on an artifact
  kilogram (IPK)
c
m (K)
 (fth Cs)


Tpta
M (12C)
Kcd

## Slide 18: International System of Units
Uncertainty Values in 2018 - before 26th General Conference on Weights and Measures
− metre: speed of light in vacuum
⇒ numerical value of the speed of light c
mechanical quantities
− kilogram: prototype of iridium platinum
mechanical quantities
− second: atomic cesium clock
10-11
10-9
1 ns
− ampere: implementation of Laplace's law
⇒ magnetic permeability in vacuum μ0
electrical quantities
⇒ quantum standards KJ e RK
− kelvin: triple point of pure water
thermal quantities
− mole: number of atoms in 0,012 kg of 12C
physicochemical, chemistry, biochemistry, biology
− candela: spectra for human vision
photometric and radiometric quantities
10-7
10-8
1 μK
10-8
10-4
A
cd
K
mol
m
kg
s
c
m (K)
 (fth Cs)

Tpta
M (12C)
Kcd