## Slide 1: Tema Metrologia cuantică
Company Name

## Slide 2: The new SI
kilogram
metre
second
ampere
kelvin
candela
mole
the Planck constant h is 6,626 070 15 × 10−34 J s
the speed of light in vacuum c is 299 792 458 m/s
the unperturbed ground state hyperfine transition frequency of the cesium 133 atom ΔνCs is 9 192 631 770 Hz
the elementary charge e is 1,602 176 634 × 10−19 C,
the Boltzmann constant k is 1,380 649 × 10−23 J/K,
the luminous efficacy of monochromatic radiation of frequency 540 × 1012 Hz, Kcd, is 683 lm/W
the Avogadro constant NA is 6,022 140 76 × 1023 mol−1
Since May 20, 2019 - The International System of Units, the SI, is the system of units in which: the 7 constants are chosen in such a way that any unit of the SI can be written either through a defining constant itself or through products or quotients of defining constants
The numerical values of the seven defining constants have no uncertainty!

## Slide 3: The new SI
kilogram
metre
second
ampere
kelvin
candela
mole
Practical Realization of Base Units
In the new formulation of the SI, the definitions allow the use of new methods for the practical realization of units - instead of each definition specifying a particular condition or physical state, which established a fundamental limit for the accuracy of the realization  it is now possible choose any equation of physics that links the respective fundamental constants to the quantity to be measured!
Different Realizations - the new definitions are not limited to a single technique  future developments may allow different ways of realizing units with better accuracy - in principle, there is no limit to the accuracy with which a unit can be implemented!

## Slide 4: The new SI
kilogram
metre
second
ampere
kelvin
candela
mole
Practical Realization of Base Units
Quantum Standards
Josephson Voltage Standard
+
Quantum Hall Resistance
Single Electron Tunnelling
Kibble
Balance
Josephson Effect
Quantum Hall Effect

## Slide 5: The new SI – Practical Realisation of kilogram
𝟏 𝐤𝐠 =
𝒉
𝟔, 𝟔𝟐𝟔 𝟎𝟕𝟎 𝟏𝟓 𝐱 10−34
𝐦 − 𝟐 𝐬 =
(299 792 458)2
(6,626 070 15 x 10−34 ) (9 192 631 770)
h ∆νCs c2
≈ 𝟏, 𝟒𝟕𝟓 𝟓𝟐𝟏𝟒 𝒙 10 40
h ∆𝝂𝑪𝒔
𝒄𝟐
The number chosen for the numerical value of the Planck constant in this definition is such that at the time of its adoption, the kilogram was equal to the mass of the international prototype, m(K) = 1 kg, with a relative standard uncertainty of 1 × 10−8 (which was the best standard uncertainty of the combined best uncertainties of the Planck constant)
Practical Realization of Base Units - kilogram
Previous definition
The kilogram is the unit of mass; it is equal to the mass of the international prototype of the kilogram (IPK). It follows that the mass of the international prototype of the kilogram is always 1 kilogram exactly, m(K) = 1 kg.
(3rd CGPM, 1901)
26th CGPM - 2018
The kilogram, symbol kg, is the SI unit of mass. It is defined by taking the fixed numerical value of the Planck constant h = 6,626 070 15 × 10−34 when
expressed in the unit J s, which is equal to kg m2 s− 1, where the metre and the second are defined in terms of c and ΔνCs.
h = 6,626 070 15 × 10−34 kg m2 s-1

## Slide 6: The new SI – Practical Realisation of kilogram
In the past few decades, significant efforts have been made to link the unit of mass to a fundamental constant of physics with high accuracy:
Crystalline silicon sphere
Practical Realization of Base Units - kilogram
The primary realization of the kilogram can be performed using any physics equation that relates mass, Planck's constant, the speed of light in a vacuum and the frequency transition of the 133Cs atom
x-ray crystal density technique
(to determine Avogadro constant NA)
Kibble balance
(to measured Planck constant h)

## Slide 7: The new SI – Practical Realisation of kilogram
Practical Realization of Base Units - kilogram
Electrical Power  Mechanical Power
Two Phases
Static phase: weighing of the artefact
(that we want to determine the respective mass)
Dynamic phase: determination of a movement
BIPM relative standard uncertainty for realizing the new kilogram definition using Kibble balance  5  10-8

## Slide 8: The new SI – Practical Realisation of kilogram
Practical Realization of Base Units - kilogram
Static phase: weighing of the artefact
m g = I L B
In a perfect alignment of the system
 Balance between
Laplace force (a coil of length L in which flows a current I when the coil is immersed in a magnetic field B)
Gravitational force (weight m · g of a
standard mass m
subject to a gravitational acceleration g)
horizontal and circular coil
horizontal and radial magnetic field

## Slide 9
Practical Realization of Base Units - kilogram
Dynamic phase: determination of a movement
the coil is moved at a vertical velocity  in the same
magnetic field B
U =  L B
U I = m g v
U =  L B
m g = I L B
h 1
i 4 gv
n2 f 2
R gv
1
U 2
m  
 

Equality of Mechanical and
Electrical Power
U = hf / 2e  Josephson Effect
R = h / e2  Quantum Hall Effet
GaAs / AlGaAs Heterostructures
Graphene samples (Nobel Prize Physics 2010)
Josephson junctions' array
SINIS (supercondutor - isolador - metal normal - isolador – supercondutor)
The new SI – Practical Realisation of kilogram

## Slide 10: The new SI – Josephson Effect
V
Tunnel barrier (Isolator)
Superconductor
(metal)
f
SIS - Nb /Al2O3 /Nb
I
 mV
Superconductor
(metal)
Josephson Effect – observed in 1962 by Brian Josephson (Nobel Prize in Physics in 1973) - allows to base the representation of the volt in terms of fundamental constants
Superconducting electrodes are separated by a tiny gap or insulating layer ( nm)  Josephson junction
Cooled below their transition temperature (~ 4,2 K)
Exposed to microwave radiation with a frequency f and a bias I applied
Superconducting state  formation of pairs of electrons – Cooper pairs
 responsible for the existence of a superconducting current

 V dt
h
I  I c sen 
 4e  
f ≈ 70 GHz
0
Corrente (mA)
Tensão (V)
-300 -150 0 150 300
Ic
empo
 
IJ
f ≈ 70 GHz
I < Ic  zero voltage in the junction terminals
Continuous Josephson Effect
I > Ic  voltage V in the junction terminals and a current oscillation of electron pairs IJ at frequency f
Alternate Josephson Effect
Current (mA)
Voltage (µV)
T Time
changing the polarization current  IJ synchronizes with f
“quantized” voltage develops across the junction  f

## Slide 11: The new SI – Josephson Effect
Josephson constant - 1990 18th CGPM
597,9  0,2 ) GHz/V
h
K  2e (483
J 90
J 90
J
2e K
n f
V (n)  n f h 
Shapiro steps
Curve V / I
f = 75 GHz - difference between two adjacent voltage
steps  155 µV
Quantized voltage - voltage steps for multiple integers
of V - proportional to the frequency of the radiation
Typical uncertainty  10-10
Typical uncertainty  10-10
creates high-precision voltage standards

## Slide 12: The new SI – Quantum Hall Effect
ie2
H
 h
i
 RK 90
I
R (i)  VH
Electrical Resistance
I
Hall resistance
V
Rxx  xx
 (25 812,807  0,005 ) 
h
RK 90  2
e
von Klitzing Constant
2 DEG existing in the interface semiconductor-semiconductor or in the semiconductor-isolator Si – MOSFET or Heterostructures GaAs / Ga Al As
Low temperatures ( 1 K)
High magnetic field ( 10 tesla)
DC Current  µA
Vxx
B
V
H
ISD
x
y
z
+
+
+
-
-
-
-
+
+
+
z
w
S
D
+
L
+
Quantum Hall Effect – discovered 1980 by Klaus von Klitzing (Nobel Prize in Physics in 1985) - allows to base the representation of the ohm in terms of fundamental constants
It is characterized by the Hall resistance being quantized into precise, discrete plateaus defined only by fundamental constants (h/e^2) and integer or fractional values, enabling a worldwide standard for resistance

## Slide 13: The new SI – Quantum Hall Effect
-5.000E+02
0.000E+00
5.000E+02
1.000E+03
1.500E+03
2.000E+03
2.500E+03
3.000E+03
3.500E+03
0.000E+00
2.000E+03
4.000E+03
6.000E+03
8.000E+03
1.000E+04
1.200E+04
1.400E+04
1.600E+04
0
2
4
6
B (tesla)
8
10
12
Rxx ( )
RH ( )
i = 2
i = 4
i = 6
Rxx oscila em função de B-1
Oscilações de Shubnikov-de-Hass
Hall resistance
H
I i ie2
R (i)  VH  RK 90  h
RH (i  1)  RK 90  (25 812,807  0,005) Ω
8 604,269 Ω
6 453,202 Ω
4 302,134 Ω
H
RH (3) 
RH (4) 
RH (6) 
R (2)  12 906,404 Ω
Ratio of RH in 2 followed steps :
RH N   N 1
RH N 1 N
Typical uncertainty  10-9

## Slide 14: The new SI – Fractional Quantum Hall Effect
In 1982, Tsui, Stormer e Laughlin
using GaAs/AlxGa1-xAs heterostructures
with high mobility values
T ≈ 0,1 K and B ≈ 20 T
observed new step of Hall resistance = 3 x RK
(i = 1/3)
T = 0,15 K e B > 5 T : Rxy corresponding to a Landau fill levels for i = 1/3, 2/5, 3/5, 2/3, 4/3 e 5/3
Limitations :
The accuracy of RH in the fractional steps is still very low for metrological applications
(for i = 1/3 the accuracy is  some parts 10-5, with B = 20 Te T = 150 mK

## Slide 15: The new SI – Quantum Hall Samples
2DEG
(3 x 1,1) mm
GaAs
n-AlGaAs
p-GaAs
2DEG
600 nm
400 nm
10 nm
1 mm
AuGeNi contacts
Substrato GaAs
z
350-500 mm
GaAs / AlGaAs Heterostructures
2 DEG is located in the inversion layer formed at the interface between two semiconductors - AlGaAs as an insulator. This thin layer is formed by electrostatic gating or bandgap engineering
Si – MOSFET
Substrate Si, doped type p (impurities - holes), allows the isolation of voltage Vg.
The contact area de (source S and drain D) is strongly doped type n+ (electrons), promoting the formation of ohmic contact to 2DEG.
A B B
A
A
B
A
B
QHARS – Quantum Hall Array Resistance Standard
series or in parallel – increasing the range of ohmic values by a single
Hall sample
between 100  e 10 M
allowing to use higher current values
Graphene samples (Nobel Prize Physics 2010)
Two-dimensional carbon crystals - By means of flip-chip technology, the graphene-based quantum resistance standards (from PTB) can be sealed to maintain constant properties even in changing environments and over long periods of time.
PTB flip-chip encapsulation of a graphene-based electric quantum resistance standard

## Slide 16: The new SI – Practical Realisation of ampere
Previous definition
The ampere is that constant current which, if maintained in two straight parallel conductors of infinite length, of negligible circular cross-section, and placed 1 metre apart in vacuum, would produce between these conductors a force equal to 2 × 10-7 newton per metre of length.
(9th CGPM, 1948)
26th CGPM - 2018
The ampere, symbol A, is the SI unit of electric current. It is defined by taking the fixed numerical value of the elementary charge e to be 1,602 176 634×10−19 when expressed in the unit C, which is equal to A s, where the second is defined in terms of ΔνCs.
e = 1,602 176 634 × 10-19 A s
𝟏 𝐀 =
𝒆
𝟏, 𝟔𝟎𝟐 𝟏𝟕𝟔 𝟔𝟑𝟒𝟏𝟎 − 𝟏𝟗
𝐬 − 𝟏 =
1
9 192 631 770 1,602 176 63410 − 19
𝐶𝑠
∆𝜈 𝑒
≈ 𝟔, 𝟕𝟖𝟗 𝟔𝟖𝟕  𝟏𝟎𝟖 ∆𝝂𝑪𝒔 𝒆

## Slide 17: The new SI – Practical Realisation of ampere
SET allows to control the charge transfer and “producing” quantified current
ISET = n  QX  f  n  e  f
f  frequency
n = 1 or 2 (1 electron / Copper pair)
QX  estimate of the elementary charge e
Typical Results:  fmax ∼ 1 GHz  Imax ∼ 160 pA
Metrology needs I ∼ 1 μA
Limitations  low current values and high uncertainty ( ± 10-7 )
Single-electron transport (SET)
SET devices
- allows the most direct unit realization of ampere using the physical
definition of current and to count individual electrons with a tiny device
Single Electron Transport device (source NIST)

## Slide 18: The Quantum Metrological Triangle
The combination of three electrical quantum effects JE - QHE – SET is called "Quantum Metrological Triangle“ - provides the accuracy of three quantum standards in the electrical domain
Josephson Effect:
VJVS = n  fJ / KJ
RQHR = RK / i
Quantum Hall Effect:
Single Electron Tunnelling:
ISET = QS fS
 2e
h
K
J
e2
K
 h
R
S
Q = e
Josephson
Effect
Quantum Hall Effect
Single-electron transport
h
KJ 
? 2e
S
Q = e
?
e2
? h
K
R
Ohm's law V = R I
J
K i
nJ f J RK
 QS f S
S
f
f J
nJ i  KJ RK QS
 1 quantitiesinteger numthatberscananbed frequantifieduq encies –
experimentally with very high accuracy
f
f J
1
n i
2 J
S
exp  the deviation from equality
uexp  associated standard uncertainty
= 1
Experimental realization of QMT - Evaluates the consistency of the constants KJ - RK - QX
1 = 1 + exp ± uexp