## Slide 1: Chapter 11: It’s a Network
Introduction to Networking
Notes: Cisco Networking Academy program
Introduction to Networking
Chapter 11: It’s a Network

## Slide 2: Chapter 11
11.0 Introduction
11.1 Create and Grow
11.2 Keeping the Network Safe
11.3 Basic Network Performance
11.4 Managing IOS Configuration Files
11.5 Integrated Routing Services
11.6 Summary
Notes: Chapter 11

## Slide 3: Chapter 11: Objectives
Upon completion of this chapter, you will be able to:
Identify the devices and protocols used in a small network.
Explain how a small network serves as the basis of larger networks.
Describe the need for basic security measures on network devices.
Identify security vulnerabilities and general mitigation techniques.
Configure network devices with device hardening features to mitigate security threats.
Use the output of ping and tracert commands to establish relative network performance.
Use basic show commands to verify the configuration and status of a device interface.

## Slide 4: Chapter 11: Objectives (Cont.)
Use the basic host and IOS commands to acquire information about the devices in a network.
Explain the file systems on Routers and Switches.
Apply the commands to back up and restore an IOS configuration file.

## Slide 5: 11.1 Create and Grow
Notes: 11.1 Create and Grow

## Slide 6: Devices in a Small Network Small Network Topologies
Typical Small Network Topology
Notes: 11.1.1.1 Small Network Topologies

## Slide 7: Devices in a Small Network Device Selection for a Small Network
Factors to be considered when selecting intermediate devices.
Notes: 11.1.1.2 Device Selection for a Small Network

## Slide 8: Devices in a Small Network IP Addressing for a Small Network
IP addressing scheme should be planned, documented and maintained based on the type of devices receiving the address.
Examples of devices that will be part of the IP design:
  End devices for users
  Servers and peripherals
  Hosts that are accessible from the Internet
  Intermediary devices
Planned IP schemes help the administrator:
  Track devices and troubleshoot
  Control access to resources
Notes: 11.1.1.3 IP Addressing for a Small Network

## Slide 9: Devices in a Small Network Redundancy in a Small Network
Redundancy helps to eliminate single points of failure.
Improves the reliability of the network.
Notes: 11.1.1.4 Redundancy in a Small Network

## Slide 10: Devices in a Small Network Design Considerations for a Small Network
The following should be included in the network design:
  Secure file and mail servers in a centralized location.
  Protect the location by physical and logical security measures.
  Create redundancy in the server farm.
  Configure redundant paths to the servers.
Notes: 11.1.1.5 Design Considerations for a Small Network

## Slide 11: Protocols in a Small Network Common Applications in a Small Network
Network-Aware Applications – Software programs that are used to communicate over the network.
Application Layer Services – Programs that interface with the network and prepare the data for transfer.
Notes: 11.1.2.1 Common Applications in a Small Network

## Slide 12: Protocols in a Small Network Common Protocols in a Small Network
Network Protocols Define:
  Processes on either end of a communication session.
  Types of messages.
  Syntax of the messages.
  Meaning of informational fields.
  How messages are sent and the expected response.
  Interaction with the next lower layer.
Notes: 11.1.2.2 Common Protocols in a Small Network

## Slide 13: Protocols in a Small Network Real-Time Applications for a Small Network
Real-time applications require planning and dedicated services to ensure priority delivery of voice and video traffic.
Infrastructure – Needs to be evaluated to ensure it will support proposed real time applications.
VoIP – Is implemented in organizations that still use traditional telephones.
IP telephony – The IP phone itself performs voice-to-IP conversion.
Real-time Video Protocols – Use Time Transport Protocol (RTP) and Real-Time Transport Control Protocol (RTCP).
Notes: 11.1.2.3 Real-Time Applications for a Small Network

## Slide 14: Growing to Larger Networks Scaling a Small Network
Important considerations when growing to a larger network:
Documentation –Physical and logical topology.
Device inventory – List of devices that use or comprise the network.
Budget – Itemized IT expense items, including the amount of money allocated to equipment purchase for that fiscal year.
Traffic Analysis – Protocols, applications, and services and their respective traffic requirements should be documented.
Notes: 11.1.3.1 Scaling a Small Network

## Slide 15: Growing to Larger Networks Protocol Analysis of a Small Network
Information gathered by protocol analysis can be used to make decisions on how to manage traffic more efficiently.
Notes: 11.1.3.2 Protocol Analysis of a Small Network

## Slide 16: Growing to Larger Networks Evolving Protocol Requirements
Network administrator can obtain IT “snapshots” of employee application utilization.
Snapshots track network utilization and traffic flow requirements.
Snapshots help inform network modifications needed.
Notes: 11.1.3.3 Evolving Protocol Requirements

## Slide 17: 11.2 Keeping the Network Safe
Notes: 11.2 Keeping the Network Safe

## Slide 18: Network Device Security Measures Threats to Network Security
Categories of Threats to Network Security
Notes: 11.2.1.1 Categories of Threats to Network Security

## Slide 19: Network Device Security Measures Physical Security
Four classes of physical threats are:
Hardware threats – Physical damage to servers, routers, switches, cabling plant, and workstations
Environmental threats – Temperature extremes (too hot or too cold) or humidity extremes (too wet or too dry)
Electrical threats – Voltage spikes, insufficient supply voltage (brownouts), unconditioned power (noise), and total power loss
Maintenance threats – Poor handling of key electrical components (electrostatic discharge), lack of critical spare parts, poor cabling, and poor labeling
Notes: 11.2.1.2 Physical Security

## Slide 20: Network Device Security Measures Types of Security Vulnerabilities
Types of Security Weaknesses:
Technological
Configuration
Security policy
Vulnerabilities - Technology
Notes: 11.2.1.3 Types of Security Vulnerabilities

## Slide 21: Vulnerabilities and Network Attacks Viruses, Worms and Trojan Horses
Virus – Malicious software that is attached to another program to execute a particular unwanted function on a workstation.
Trojan horse – An entire application written to look like something else, when in fact it is an attack tool.
Worms – Worms are self-contained programs that attack a system and try to exploit a specific vulnerability in the target. The worm copies its program from the attacking host to the newly exploited system to begin the cycle again.
Notes: 11.2.2.1 Viruses, Worms and Trojan Horses

## Slide 22: Vulnerabilities and Network Attacks Reconnaissance Attacks
Notes: 11.2.2.2 Reconnaissance, Access and DoS Attacks

## Slide 23: Vulnerabilities and Network Attacks Access Attacks
Notes: 11.2.2.3 Access Attacks

## Slide 24: Vulnerabilities and Network Attacks Access Attacks (Cont.)
Notes: 11.2.2.3 Access Attacks

## Slide 25: Vulnerabilities and Network Attacks Denial of Service Attacks (DoS)
Notes: 11.2.2.4 DoS Attacks

## Slide 26: Mitigating Network Attacks Backup, Upgrade, Update, and Patch
Keep current with the latest versions of antivirus software.
Install updated security patches.
Antivirus software can detect most viruses and many Trojan horse applications and prevent them from spreading in the network.
Notes: 11.2.3.1 Backup, Upgrade, Update, and Patch

## Slide 27: Mitigating Network Attacks Authentication, Authorization, and Accounting
Authentication, Authorization, and Accounting (AAA, or “triple A”)
Authentication – Users and administrators must prove their identity. Authentication can be established using username and password combinations, challenge and response questions, token cards, and other methods.
Authorization – Determines which resources the user can access and the operations that the user is allowed to perform.
Accounting – Records what the user accessed, the amount of time the resource is accessed, and any changes made.
Notes: 11.2.3.2 Authentication, Authorization, and Accounting

## Slide 28: Mitigating Network Attacks Firewalls
A Firewall resides between two or more networks. It controls traffic and helps prevent unauthorized access.
Methods used are:
Packet Filtering
Application Filtering
URL Filtering
Stateful Packet Inspection (SPI) – Incoming packets must be legitimate responses to requests from internal hosts.
Firewalls
Notes: 11.2.3.3 Firewalls

## Slide 29: Mitigating Network Attacks Endpoint Security
Common endpoints are laptops, desktops, servers, smart phones, and tablets.
Employees must follow the companies documented security policies to secure their devices.
Policies often include the use of anti-virus software and host intrusion prevention.
Common Endpoint Devices
Notes: 11.2.3.4 Endpoint Security

## Slide 30: Securing Devices Introduction to Securing Devices
Part of network security is securing devices, including end devices and intermediate devices.
Default usernames and passwords should be changed immediately.
Access to system resources should be restricted to only the individuals that are authorized to use those resources.
Any unnecessary services and applications should be turned off and uninstalled, when possible.
Update with security patches as they become available.
Notes: 11.2.4.1 Introduction to Securing Devices

## Slide 31: Securing Devices Passwords
Weak and Strong Passwords
Notes: 11.2.4.2 Passwords

## Slide 32: Securing Devices Basic Security Practices
Encrypt passwords.
Require minimum length passwords.
Block brute force attacks.
Use Banner Message.
Set EXEC timeout.
Securing Devices
Notes: 11.2.4.3 Basic Security Practices

## Slide 33: Securing Devices Enable SSH
Notes: 11.2.4.4 Enable SSH

## Slide 34: 11.3 Basic Network Performance
Notes: 11.3 Basic Network Performance

## Slide 35: Ping Interpreting ICMP Messages
! – indicates receipt of an ICMP echo reply message
. – indicates a time expired while waiting for an ICMP echo reply message
U – an ICMP unreachable message was received
Notes: 11.3.1.1 Interpreting ICMP Messages

## Slide 36: Ping Leveraging Extended Ping
The Cisco IOS offers an "extended" mode of the ping command:
  R2# ping
  Protocol [ip]:
  Target IP address: 192.168.10.1
  Repeat count [5]:
  Datagram size [100]:
  Timeout in seconds [2]:
  Extended commands [n]: y
  Source address or interface: 10.1.1.1
  Type of service [0]:
Notes: 11.3.1.2 Leveraging Extended Ping

## Slide 37: Ping Network Baseline
Baseline with ping
Notes: 11.3.1.3 Network Baseline

## Slide 38: Ping Network Baseline (Cont.)
Notes: 11.3.1. 3 Network Baseline (Cont.)

## Slide 39: Tracert Interpreting Tracert Messages
Notes: 11.3.2.1 Interpreting Tracert Messages

## Slide 40: Show Commands Common Show Commands Revisited
The status of nearly every process or function of the router can be displayed using a show command.
Frequently used show commands:
  show running-config
  show interfaces
  show arp
  show ip route
  show protocols
  show version
Notes: 11.3.3.1 Common Show Commands Revisited

## Slide 41: Show Commands Viewing Router Settings With Show Version
Cisco IOS Version
System Bootstrap
Cisco IOS Image
CPU and RAM
Configuration Register
Number and Type of Physical Interfaces
Amount of NVRAM
Amount of Flash
Notes: 11.3.3.2 Viewing Router Settings with the Show Version Command

## Slide 42: Show Commands Viewing Switch Settings With Show Version
show version Command
Notes: 11.3.3.3 Viewing Switch Settings with Show Version

## Slide 43: Host and IOS Commands ipconfig Command Options
ipconfig – Displays ip address, subnet mask, default gateway.
ipconfig /all – Also displays MAC address.
ipconfig /displaydns – Displays all cached dns entries in a Windows system.
Notes: 11.3.4.1 ipconfig Command Options

## Slide 44: Host and IOS Commands arp Command Options
arp Command Options
Notes: 11.3.4.2 arp Command Options

## Slide 45: Host and IOS Commands show cdp neighbors Command Options
show cdp neighbors command provides information about each directly connected CDP neighbor device.
Notes: 11.3.4.3 Show cdp neighbors Command Options

## Slide 46: Host and IOS Commands Using show ip interface brief Command
show ip interface brief command-used to verify the status of all network interfaces on a router or a switch.
Notes: 11.3.4.4 Using the show ip interface brief Command

## Slide 47: 11.4 Managing IOS Configuration Files
Notes: 11.4 Managing IOS Configuration Files

## Slide 48: Router and Switch File Systems Router File Systems
show file systems command – Lists all of the available file systems on a Cisco 1941 route.
The asterisk (*) indicates this is the current default file system.
Notes: 11.4.1.1 Router File Systems

## Slide 49: Router and Switch File Systems Switch File Systems
show file systems command – Lists all of the available file systems on a Catalyst 2960 switch.
Notes: 11.4.1.2 Switch File Systems

## Slide 50: Backup and Restore Configuration Files Backup and Restore Using Text Files
Saving to a Text File in Tera Term
Notes: 11.4.2.1 Backing up and Restore using Text Files

## Slide 51: Backup and Restore Configuration Files Backup and Restore Using TFTP
Configuration files can be stored on a Trivial File Transfer Protocol (TFTP) server.
copy running-config tftp – Save running configuration to a tftp server.
copy startup-config tftp – Save startup configuration to a tftp server.
Notes: 11.4.2.2 Backing up and Restore using TFTP

## Slide 52: Backup and Restore Configuration Files Using USB Interfaces on a Cisco Router
USB flash drive must be formatted in a FAT16 format.
Can hold multiple copies of the Cisco IOS and multiple router configurations.
Allows administrator to easily move configurations from router to router.
Notes: 11.4.2.3 Using USB Interfaces on a Cisco Router

## Slide 53: Backup and Restore Configuration Files Backup and Restore Using USB
Backup to USB Drive
Notes: 11.4.2.4 Backup and Restore Using USB

## Slide 54: 11.5 Integrated Routing Services
Notes: 11.5 Integrated Routing Services

## Slide 55: Integrated Router Multi-function Device
Multi-function Device
Incorporates a switch, router, and wireless access point.
Provides routing, switching and wireless connectivity.
Linksys wireless routers, are simple in design and used in home networks
Cisco Integrated Services Router (ISR) product family offers a wide range of products, designed for small office to larger networks.
Notes: 11.5.1.1 Multi-function device
11.5.1.2 Types of Integrated Routers

## Slide 56: Integrated Router Wireless Capability
Wireless Mode – Most integrated wireless routers support 802.11b, 802.11g and 802.11n.
Service Set Identifier (SSID) – Case-sensitive, alpha-numeric name for your home wireless network.
Wireless Channel – RF spectrum can be divided up into channels.
Linksys Wireless Settings
Notes: 11.5.1.3 Wireless Capability

## Slide 57: Integrated Router Basic Security of Wireless
Change default values
Disable SSID broadcasting
Configure Encryption using WEP or WPA
Wired Equivalency Protocol (WEP) - Uses pre-configured keys to encrypt and decrypt data. Every wireless device allowed to access the network must have the same WEP key entered.
Wi-Fi Protected Access (WPA) – Also uses encryption keys from 64 bits up to 256 bits. New keys are generated each time a connection is established with the AP; therefore, more secure.
Notes: 11.5.1.4 Basic Security of Wireless

## Slide 58: Integrated Router Configuring the Integrated Router
Step 1 - Access the router by cabling a computer to one of the router’s LAN Ethernet ports.
Step 2 - The connecting device will automatically obtain IP addressing information from Integrated Router.
Step 3 - Change default username and password and the default Linksys IP address for security purposes.
Initial Access to the Router
Notes: 11.5.2.1 Configuring the Integrated Router

## Slide 59: Integrated Router Enabling Wireless
Step 1 - Configure the wireless mode
Step 2 - Configure the SSID
Step 3 - Configure RF channel
Step 4 - Configure any desired security encryption
Notes: 11.5.2.2 Enabling Wireless

## Slide 60: Integrated Router Configure a Wireless Client
The wireless client configuration settings must match that of the wireless router.
  SSID
  Security Settings
  Channel
Wireless client software can be integrated into the device operating system or stand alone, downloadable, wireless utility software.
Notes: 11.5.2.3 Configure a Wireless Client

## Slide 61: 11.6 Summary
Notes: 11.6 Summary

## Slide 62: Chapter 11: Summary
In this chapter, you learned:
Good network design incorporates reliability, scalability, and availability.
Networks must be secured from viruses, Trojan horses, worms and network attacks.
The importance of documenting Basic Network Performance.
How to test network connectivity using ping and traceroute.
How to use IOS commands to monitor and view information about the network and network devices.
How to backup configuration files using TFTP or USB.
Home networks and small business often use integrated routers, which provide the functions of a switch, router and wireless access point.
Notes: 11.6 Summary