## Slide 1: Chapter 3: Network Protocols and Communications
Introduction to Networks
Notes: Cisco Networking Academy program
Introduction to Networks
Chapter 3: Network Protocols and Communications

## Slide 2: Chapter 3: Objectives
After completing this chapter, you will be able to:
Explain how rules are used to facilitate communication.
Explain the role of protocols and standards organizations in facilitating interoperability in network communications.
Explain how devices on a LAN access resources in a small to medium-sized business network.
Notes: 2

## Slide 3: Chapter 3
  3.1 Rules of Communication
  3.2 Network Protocols and Standards
  3.3 Moving Data in the Network
  3.4 Summary
Notes: Chapter 3 Sections

## Slide 4: 3.1 Rules of Communication
Notes: Cisco Networking Academy program
Introduction to Networks
Chapter 3: Network Protocols and Communications

## Slide 5: The Rules What is Communication?
Notes: 3.1.1.1 What is Communication?

## Slide 6: The Rules Establishing the Rules
An identified sender and receiver
Agreed upon method of communicating (face-to-face, telephone, letter, photograph)
Common language and grammar
Speed and timing of delivery
Confirmation or acknowledgment requirements
Notes: 3.1.1.2 Establishing the Rules

## Slide 7: The Rules Message Encoding
Notes: 3.1.1.3 Message Encoding

## Slide 8: The Rules Message Formatting and Encapsulation
Example: Personal letter contains the following elements:
Identifier of the recipient’s location
Identifier of the sender’s location
Salutation or greeting
Recipient identifier
The message content
Source identifier
End of message indicator
Notes: 3.1.1.4 Message Formatting and Encapsulation

## Slide 9: The Rules Message Size
An overview of the segmenting process:
The size restrictions of frames require the source host to break a long message into individual pieces (or segments) that meet both the minimum and maximum size requirements.
Each segment is encapsulated in a separate frame with the address information, and is sent over the network.
At the receiving host, the messages are de-encapsulated and put back together to be processed and interpreted.
Notes: 3.1.1.5 Message Size

## Slide 10: The Rules Message Timing
Access Method
Flow Control
Response Timeout
Notes: 3.1.1.6 Message Timing

## Slide 11: The Rules Message Delivery Options
Notes: 3.1.1.7 Message Delivery Options

## Slide 12: 3.2 Network Protocols and Standards
Notes: Cisco Networking Academy program
Introduction to Networks
Chapter 3: Network Protocols and Communications

## Slide 13: Protocols Rules that Govern Communications
Notes: 3.2.1.1 Protocols: Rules that Govern Communications

## Slide 14: Protocols Network Protocols
How the message is formatted or structured
The process by which networking devices share information about pathways with other networks
How and when error and system messages are passed between devices
The setup and termination of data transfer sessions
Notes: 3.2.1.2 Network Protocols

## Slide 15: Protocols Interaction of Protocols
Application Protocol – Hypertext Transfer Protocol (HTTP)
Transport Protocol – Transmission Control Protocol (TCP)
Internet Protocol – Internet Protocol (IP)
Network Access Protocols – Data link & physical layers
Notes: 3.2.1.3 Interaction of Protocols

## Slide 16: Protocol Suites Protocol Suites and Industry Standards
Notes: 3.2.2.1 Protocol Suites and Industry Standards

## Slide 17: Protocol Suites Creation of Internet, Development of TCP/IP
The first packet switching network and predecessor to today’s Internet was the Advanced Research Projects Agency Network (ARPANET), which came to life in 1969 by connecting mainframe computers at four locations.
ARPANET was funded by the U.S. Department of Defense for use by universities and research laboratories. Bolt, Beranek and Newman (BBN) was the contractor that did much of the initial development of the ARPANET, including creating the first router known as an Interface Message Processor (IMP).
In 1973, Robert Kahn and Vinton Cerf began work on TCP to develop the next generation of the ARPANET. TCP was designed to replace ARPANET’s current Network Control Program (NCP).
In 1978, TCP was divided into two protocols: TCP and IP. Later, other protocols were added to the TCP/IP suite of protocols including Telnet, FTP, DNS, and many others.
Notes: 3.2.2.2 Creation of the Internet and Development of TCP/IP

## Slide 18: Protocol Suites TCP/IP Protocol Suite and Communication
Notes: 3.2.2.3 TCP/IP Protocol Suite and Communication Process

## Slide 19: Standards Organizations Open Standards
The Internet Society (ISOC)
The Internet Architecture Board (IAB)
The Internet Engineering Task Force (IETF)
Institute of Electrical and Electronics Engineers (IEEE)
The International Organization for Standards (ISO)
Notes: 3.2.3.1 Open Standards

## Slide 20: Standards Organizations ISOC, IAB, and IETF
Notes: 3.2.3.2 ISOC, IAB, and IETF

## Slide 21: Standards Organizations IEEE
38 societies
130 journals
1,300 conferences each year
1,300 standards and projects
400,000 members
160 countries
IEEE 802.3
IEEE 802.11
Notes: 3.2.3.3 IEEE

## Slide 22: Standards Organizations ISO
OSI Model
Notes: 3.2.3.4 ISO

## Slide 23: Standards Organizations Other Standards Organization
The Electronic Industries Alliance (EIA)
The Telecommunications Industry Association (TIA)
The International Telecommunications Union – Telecommunications Standardization Sector (ITU-T)
The Internet Corporation for Assigned Names and Numbers (ICANN)
The Internet Assigned Numbers Authority (IANA)
Notes: 3.2.3.5 Other Standards Organizations

## Slide 24: Reference Models Benefits of Using a Layered Model
Notes: 3.2.4.1 The Benefits of Using a Layered Model

## Slide 25: Reference Models The OSI Reference Model
Notes: 3.2.4.2 The OSI Reference Model

## Slide 28: Reference Models The TCP/IP Reference Model
Notes: 3.2.4.3 The TCP/IP Protocol Model

## Slide 29: Reference Models Comparing the OSI and TCP/IP Models
Notes: 3.2.4.4 Comparing the OSI Model with the TCP/IP Model

## Slide 30: 3.3 Moving Data in the Network
Notes: Cisco Networking Academy program
Introduction to Networks
Chapter 3: Network Protocols and Communications

## Slide 31: Data Encapsulation Communicating the Messages
Segmenting message benefits
  Different conversations can be interleaved
  Increased reliability of network communications
Segmenting message disadvantage
  Increased level of complexity
Notes: 3.3.1.1 Communicating the Messages

## Slide 32: Data Encapsulation Protocol Data Units (PDUs)
Data
Segment
Packet
Frame
Bits
Notes: 3.3.1.2 Protocol Data Units (PDUs)

## Slide 33: Data Encapsulation Protocol Encapsulation
Notes: 3.3.1.3 Encapsulation

## Slide 34: Data Encapsulation Protocol De-encapsulation
Notes: 3.3.1.4 De-encapsulation

## Slide 35: Moving Data in the Network Accessing Local Resources
Notes: 3.3.2.1 Network Addresses and Data Link addresses

## Slide 36: Accessing Local Resources Communicating with Device / Same Network
Notes: 3.3.2.2 Communicating with a Device on the Same Network

## Slide 37: Accessing Local Resources MAC and IP Addresses
PC1
192.168.1.110
AA-AA-AA-AA-AA-AA
PC2
192.168.1.111
BB-BB-BB-BB-BB-BB
FTP Server
192.168.1.9
CC-CC-CC-CC-CC-CC
R1
192.168.1.1
11-11-11-11-11-11
ARP
Request
S1
R1
Notes: 3.3.2.3 MAC and IP Addresses

## Slide 38: Accessing Remote Resources Default Gateway
Notes: 3.3.3.1 Default Gateway

## Slide 39: Accessing Remote Resources Communicating Device / Remote Network
Notes: 3.3.3.2 Communicating with a Device on a Remote Network

## Slide 40: Network Protocols and Communications Summary
In this chapter, you learned:
Data networks are systems of end devices, intermediary devices, and the media connecting the devices. For communication to occur, these devices must know how to communicate.
These devices must comply with communication rules and protocols. TCP/IP is an example of a protocol suite.
Most protocols are created by a standards organization such as the IETF or IEEE.
The most widely-used networking models are the OSI and TCP/IP models.
Data that passes down the stack of the OSI model is segmented into pieces and encapsulated with addresses and other labels. The process is reversed as the pieces are de-encapsulated and passed up the destination protocol stack.
Notes: Chapter 3 Summary

## Slide 41: Network Protocols and Communications Summary (cont.)
In this chapter, you learned:
The OSI model describes the processes of encoding, formatting, segmenting, and encapsulating data for transmission over the network.
The TCP/IP protocol suite is an open standard protocol that has been endorsed by the networking industry and ratified, or approved, by a standards organization.
The Internet Protocol Suite is a suite of protocols required for transmitting and receiving information using the Internet.
Protocol Data Units (PDUs) are named according to the protocols of the TCP/IP suite: data, segment, packet, frame, and bits.
Applying models allows individuals, companies, and trade associations to analyze current networks and plan the networks of the future.
Notes: Chapter 3 Summary (cont.)